## Slide 1
Adaptive Facial ROI Selection:
Full-Cohort Diagnostics
MCD evaluation update
September 2, 2026
Atharva Walawalkar
Notes: - This update reports completed MCD-only diagnostics using frozen Advantage PPO checkpoints; it does not introduce a new training result.
- The central comparison separates ROI-selection alternatives from cases where recovered ROI POS estimates do not contain GT.
- Source: `docs/diagnostics/mcd_long_term_regret.md` and `docs/diagnostics/mcd_pos_extreme_range.md`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/diagnostics/mcd_pos_extreme_range.md

## Slide 2
MCD evaluation update
01
Terms and questions for this update
Definitions
• Remote photoplethysmography (rPPG): estimating heart rate from facial video.
• MCD: the evaluation dataset used for every result in this deck; the retained cohort contains 533 clips from 89 subjects.
• Ground truth (GT): the reference heart rate used only for evaluation and offline diagnostics.
• Region of interest (ROI): one facial area used to measure the pulse signal.
• Plane-Orthogonal-to-Skin (POS): the signal-processing method that converts color changes into a heart-rate estimate.
• Hop: one controller decision point. H15 is the mean absolute error across the next 15 hops.
Questions
• Was a better ROI action available at the same state?
• Did one changed action affect later decisions across the next 15 hops?
• Was GT outside every recovered ROI estimate?
This update separates controller-selection headroom from cases where the POS estimates themselves do not bracket GT.
Notes: - The controller is a frozen recurrent Proximal Policy Optimization (PPO) model that selects one ROI at each hop.
- All GT-informed alternatives in this update are offline diagnostics, not actions available to a deployable system.
- No MMPD data were accessed or used; all reported results are from the MCD evaluation split.
- Source: `docs/diagnostics/mcd_long_term_regret.md` and `docs/diagnostics/mcd_pos_extreme_range.md`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/diagnostics/mcd_pos_extreme_range.md

## Slide 3
MCD evaluation update
02
Starting point, the frozen MCD benchmark
Method
Equal-clip MAE (BPM)
Fixed full-face POS
12.6317
Dataset Aggregation (DAgger), three-seed mean
8.4716
Standard Proximal Policy Optimization (PPO), three-seed mean
7.9913
Advantage PPO, three-seed mean
7.6232
533 clips • 89 subjects • 91,227 hops per method
Advantage PPO scored below fixed full-face POS, but the benchmark alone did not explain the remaining failures.
Notes: - Family values are arithmetic seed means, not ensembles.
- Source: `docs/gates/gate_08_mcd_frozen_models.md` and evidence-registry entry E-031.
[Sources]
- docs/gates/gate_08_mcd_frozen_models.md
- docs/evidence_registry.md, E-031

## Slide 4
MCD evaluation update
03
We built an all-action counterfactual source
Nine frozen learned models
533 evaluation clips
4,797 clip-model rows
801 subject-model rows
821,043 hop-model rows
At the same state
Factual
selection
vs.
All legal
immediate ROI
alternatives
Every hop stores the factual selection and all legal immediate ROI alternatives
This source lets us separate the ROI selected by the policy from the alternatives available at exactly the same state.
Notes: - This source reports immediate counterfactual alternatives. By itself, it is not a 15-hop regret result.
- Remote source: `/Users/924254653/mcd_failure_eval_full2_20260826/output/full-eval2-20260826/merged/`.
- `per_hop_counterfactual.csv` SHA-256: `930c1ca3cc414558d044a0f3a9bab4e49830bcc2e6e3da9ec1725b59bd68f715`.
- The source completed on 2026-08-26; its scheduler identifier is retained only in the dated verification record.
[Sources]
- /Users/924254653/mcd_failure_eval_full2_20260826/output/full-eval2-20260826/merged/
- docs/diagnostics/mcd_long_term_regret.md

## Slide 5
MCD evaluation update
04
The 15-hop diagnostic changes one decision and follows the frozen policy
1
Replay the factual PPO action.
2
Force each of the 12 ROI actions once.
3
Return control to the same frozen recurrent PPO policy.
4
Compare error over 1, 5, and 15 hops.
→
→
→
Separate repeated-correction arm:
Retain PPO and the best immediate GT-informed correction at each step.
Compare retained correction schedules over 15 hops.
The diagnostic tests downstream consequences of changed actions; the alternatives use GT offline and are not deployable policies.
Notes: - Minimum-hold constraints remain active.
- The width-8 repeated path is retained and pruned, not globally optimal.
- Source: `docs/diagnostics/mcd_long_term_regret.md` and `configs/evaluation/mcd_repeated_correction_beam_full_v1.json`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- configs/evaluation/mcd_repeated_correction_beam_full_v1.json

## Slide 6
MCD evaluation update
05
We expanded from the worst 54 clips to the full MCD cohort
Date
Diagnostic stage
Verified status
Aug. 27-28
Worst 54 clips, three seeds
162 producer tasks complete; behavioral v1 tables remain provisional
Aug. 31
Full 533 clips, seed 1
533 tasks and v2 aggregate complete
Sept. 1
Full 533 clips, seed 0
533 tasks and v2 aggregate complete
Sept. 1
Full 533 clips, seed 2
533 tasks and v2 aggregate complete
Full-cohort producer and aggregate coverage now exists for every Advantage PPO seed.
Notes: - Every seed produced 533 task summaries and passed factual parity in all 533 tasks.
- Seed 1 completed on 2026-08-31; seeds 0 and 2 completed on 2026-09-01.
- Each matching v2 aggregate completed successfully and used the same comparison tolerance and aggregation rule.
- Exact scheduler identifiers, runtimes, paths, and artifact hashes are retained in the dated verification record and `docs/diagnostics/mcd_long_term_regret.md`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/presentations/2026-09-02_research_update_materials/2026-09-02_PPT_MATERIALS.md

## Slide 7
MCD evaluation update
06
One-time correction results across three seeds
Full-cohort subject-weighted result
Seed 0
Seed 1
Seed 2
Seed mean [range]
Factual PPO H15 MAE (BPM)
7.509
7.355
7.583
7.482 [7.355, 7.583]
Positive immediate regret
64.88%
66.66%
67.12%
66.22% [64.88%, 67.12%]
Mean immediate regret (BPM)
1.498
1.509
1.604
1.537 [1.498, 1.604]
Best saved single beat factual H15
96.71%
96.68%
96.62%
96.67% [96.62%, 96.71%]
Best saved single H15 reduction (BPM)
2.113
2.114
2.310
2.179 [2.113, 2.310]
Every seed shows immediate action-selection regret and substantial retrospective one-time correction headroom.
Notes: - Positive immediate regret means a legal GT-ranked action had lower immediate error than factual PPO at the anchor.
- Best saved single is retrospective: it selects the lowest H15 MAE among saved genuine one-time deviations anywhere from X through X+14 with complete coverage.
- Seed-specific intervals and raw counts are recorded in `docs/diagnostics/mcd_long_term_regret.md`.
- Seed means and ranges are descriptive; eligible anchors are seed-specific and not matched.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md

## Slide 8
MCD evaluation update
07
Repeated-correction results across three seeds
Full-cohort subject-weighted result
Seed 0
Seed 1
Seed 2
Seed mean [range]
Repeated path beat best saved single
92.24%
89.65%
90.98%
90.96% [89.65%, 92.24%]
Repeated H15 reduction vs factual (BPM)
3.752
3.592
3.890
3.745 [3.592, 3.890]
Repeated reduction vs best single (BPM)
1.555
1.443
1.463
1.487 [1.443, 1.555]
Later PPO proposal change rate
51.10%
62.03%
60.01%
57.71% [51.10%, 62.03%]
Retained repeated corrections usually improve beyond the best saved one-time correction, and the changed measurement history often alters later PPO proposals.
Notes: - The repeated path contains at least two real legal deviations from PPO.
- It uses GT offline and a retained width-8 beam. It is neither deployable nor globally optimal.
- Aggregation: anchor mean within clip, equal clips within subject, equal subjects within seed, 10,000 subject-bootstrap draws.
- Source: `docs/diagnostics/mcd_long_term_regret.md` and the three remote v2 summaries.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- /Users/924254653/mcd_repeated_beam_full_seed0_analysis_48705_v1/
- /Users/924254653/mcd_repeated_beam_full_seed1_analysis_48580_v1/
- /Users/924254653/mcd_repeated_beam_full_seed2_analysis_48706_v1/

## Slide 9
MCD evaluation update
08
Separate diagnostic, where all recovered ROI POS estimates lie relative to GT
Combined recovery outcome
Count
Percentage
GT below the lowest valid ROI estimate
620
0.76%
GT inside the ROI estimate range
74,564
91.67%
GT above the highest valid ROI estimate
6,159
7.57%
GT outside the range
6,779
8.33%
Denominator: 81,343 clip-hops with all 12 executed ROI identities recovered and at least one valid finite HR estimate.
GT was outside the recovered ROI POS range in 8.33% of the usable complete-recovery hops, most often above every ROI estimate.
Notes: - The full source contains 91,227 clip-hops. Partial recovery and complete recovery with no valid ROI are reported separately and excluded from this denominator.
- Combined recovery uses three seeds to recover stored executed-action measurements. It is not an ensemble.
- Source: `docs/diagnostics/mcd_pos_extreme_range.md` and evidence-registry entry E-032.
[Sources]
- docs/diagnostics/mcd_pos_extreme_range.md
- docs/evidence_registry.md, E-032

## Slide 10
MCD evaluation update
09
How far outside the ROI range was GT?
Direction
n
Mean miss
Median
P90
Maximum
GT below all valid ROI estimates
620
5.3337 BPM
3.0762
12.7441
44.3848
GT above all valid ROI estimates
6,159
8.1062 BPM
5.2734
18.8965
88.3301
The dominant outside-range failure is POS underestimating GT across every recovered valid ROI.
Notes: - Counts are clip-hops, not subject-weighted prevalence.
- The maxima are rare extremes; use the median and P90 to describe the distribution.
[Sources]
- docs/diagnostics/artifacts/mcd_pos_extreme_range/extreme_range_miss_distributions.svg
- docs/diagnostics/artifacts/mcd_pos_extreme_range/extreme_range_miss_statistics.csv

## Slide 11
MCD evaluation update
10
The diagnostics answer different questions
15-hop regret diagnostic
• Is there a better action at the same state?
• Does one correction affect later PPO decisions?
• How much 15-hop headroom remains?
POS range diagnostic
• Is GT numerically reachable by any recovered ROI POS estimate?
• Is POS collectively above or below GT?
• How large are the outside-range misses?
One diagnostic measures controller/action headroom; the other measures estimator-level candidate-range failure. Neither alone explains the other.
Notes: - The regret diagnostic compares factual PPO with saved GT-informed alternatives under the same frozen controller and asks whether different selections could reduce error.
- The POS range diagnostic asks a narrower numerical question: whether GT lies between the lowest and highest recovered valid ROI estimates.
- An outside-range POS case cannot be repaired by choosing among those recovered estimates alone, but this does not prove that POS caused every PPO error.
- Source: `docs/diagnostics/mcd_long_term_regret.md` and `docs/diagnostics/mcd_pos_extreme_range.md`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/diagnostics/mcd_pos_extreme_range.md

## Slide 12
MCD evaluation update
11
What is complete and what remains before final interpretation
Complete
• Three full-cohort producer runs and matching v2 aggregates, one for each Advantage PPO seed
• Three-seed 15-hop behavioral tables with the same definitions and aggregation rule
• Three-seed POS range and miss-distribution analysis
Still separate or unresolved
• The four-case visual audit remains blocked at replay validation and provides no behavioral conclusion.
• A matched simple non-RL selection baseline could be the next comparison if it would change the research decision.
• MMPD transfer remains outside this MCD-only diagnostic update.
The planned three-seed aggregation is complete; the case-level explanation and broader baseline comparison remain separate questions.
Notes: - The full-cohort result package now contains one producer run and one matching v2 aggregate for each Advantage PPO seed.
- The four-case visual audit stopped at replay validation, so it contributes no case-level explanation to this update.
- The next comparison should be selected only if it changes the research decision; no new baseline result is claimed here.
- Source: `docs/diagnostics/mcd_long_term_regret.md`, `docs/diagnostics/mcd_pos_extreme_range.md`, and `docs/evidence_registry.md`.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/diagnostics/mcd_pos_extreme_range.md
- docs/evidence_registry.md

## Slide 13
MCD evaluation update
12
What we can discuss tomorrow
• Across seeds, 64.88% to 67.12% of eligible anchors had positive immediate regret.
• The retrospective best saved one-time deviation beat factual H15 in 96.62% to 96.71% of eligible anchors, with a subject-weighted H15 reduction of 2.113 to 2.310 BPM.
• The retained repeated path reduced H15 error versus factual by 3.592 to 3.890 BPM and changed later PPO proposals in 51.10% to 62.03% of cases.
• Separately, GT was outside the recovered ROI POS range in 8.33% of usable complete-recovery clip-hops, most often above every ROI estimate.
• These are MCD-only, GT-informed offline diagnostics. They measure available headroom but do not provide a deployable policy, prove optimality, establish transfer, or explain the internal reason PPO made a choice.
Decision requested:
Interpret the completed three-seed results together and decide whether the next priority is a matched simple selection baseline or the blocked case-level audit.
Notes: - All three seeds show the same broad pattern: frequent immediate action-selection headroom, larger retrospective 15-hop headroom, and changed later PPO proposals after some corrections.
- The separate POS result shows that 8.33% of usable complete-recovery clip-hops had GT outside the recovered ROI estimate range, with 6,159 of 6,779 outside-range cases above the highest estimate.
- The decision is whether to test the controller against a simpler matched selector next or first repair the case replay needed for human-level examples.
- Source: `docs/diagnostics/mcd_long_term_regret.md`, `docs/diagnostics/mcd_pos_extreme_range.md`, and the pinned numerical evidence at the top of this file.
[Sources]
- docs/diagnostics/mcd_long_term_regret.md
- docs/diagnostics/mcd_pos_extreme_range.md
- docs/presentations/2026-09-02_research_update_materials/2026-09-02_PPT_MATERIALS.md